## Slide 1: Daikin Visit
November 7, 2014

## Slide 2
Intervention Thermal Comfort
Airflow Measurements
Green Roof Experiment
Testing Building Materials
Testing Airflow Supplies
Indoor Air Quality
Completed Research
Notes: Previous Research

## Slide 3: Reference Facility
Built and used over 12 years at Penn State
Climate Chamber simulates outdoor conditions
Environmental Chamber represents indoor spaces
Dual HVAC systems for separate chambers, independent controls
Measurement Instruments
  Tracer Gas
  Aero Trak
  CO2 Sensors
  P-Track
  Temperature and Humidity Sensors
Notes: Penn State Facilty

## Slide 4
  15’ x 22’ x 15’
New Environmental Chamber
  Climate and Environmental Chambers
Notes: Old Facility

## Slide 5
Dual Compartments Testing Chamber
Controls
  Max time to new set response is 10 min
  Supply air change rate from 0.5 to 20 ACH
  Record measurements in real time at varying intervals
Power Availability
  208 3 Phase & 250 Amps
Max Supported Load is 2kW
  6 People, 6 PCs, lamps, and testing equipment
New Environmental Chamber
Notes: Old Facility

## Slide 6
  AHU Details
    Independent Air Cooled AHUs
    Operate with 0-100% of the outdoor air
    Design for Outdoor Air (100% OA)
      Summer 95oF 60% RH
      Winter 19.4oF 60% RH
    MERV 8 filtered blower VSD accurately supplies air for 0.5 air changes per hour
New Environmental Chamber
Notes: Old Facility

## Slide 7
  SF6 Tracer Gas
  Portable Temperature iButtons
  Handheld Aero-Trak
  Handheld P-Trak
  CO2 Sensors
  Temperature and Humidity Sensors
  Thermal Cameras
Measurement Capabilities
Notes: Old Facility

## Slide 8: Ongoing& Future research
EFRI PULSE
  Urban Modeling at Campus Level
  Energy Modeling + CFD + Solar Radiation
  Multi-Building Control Strategies
  Relations to Occupant Comfort/Health
Smart Building Experience
  Occupant feedback to building systems
  Occupant physiological responses
  Environmental Chamber tests
  Real Time Energy & Occupant Visualiation
Notes: Old Facility